## Slide 1: Probabilistic numerics at scale by distributed inference
Alex Ledbetter, Mykola Lukashchuk & Wouter Kouw
International Conference on Probabilistic Numerics 2026

## Slide 2: Outline
1
Problem specification
2
Classical numerical approach
3
Probabilistic numerical approach
4
Message passing approach
5
Stacking modular components

## Slide 3: 1. Problem statement
A
Heat transfer on a silicon die
B
Solving a system of linear equations
C
Sparsity structure of A

## Slide 4: Problem statement
This is a silicon die, specifically a Pentium II.
It contains a complete electronic circuit that performs a specific function (this one computes).
Each tile (region) draws power and heats up.
Heat spreads through the silicon material.
We want to keep the die cool, which we can do by "throttling" power consumption.
To decide which to "throttle", the control system needs the steady-state temperature of every tile.

## Slide 5: Heat transfer on the die
Let be the temperature of the -th tile, and its power consumption.
The steady-state solution of the change in temperature over time is:
where is the set of neighbors and is a parameter.
The neighbor contributions can be approximated with the Laplacian .
Then

## Slide 6: System of linear equations
We stack the tile temperatures and power consumptions:
For , the steady-state solution is .
Given a vector of power consumptions, we can calculate steady-state temperature with
tiles on one die, today | 
Graphcore IPU | 1 472
Tenstorrent Blackhole | 140
Cerebras WSE-3 | 900 000
tiles on one die, today | 
Graphcore IPU | 1 472
Tenstorrent Blackhole | 140
Cerebras WSE-3 | 900 000

## Slide 7: Sparsity structure of A
If the die is tiled as a chain, then A will be tri-diagonal.
If the die is tiled as a grid, then A will be denser.

## Slide 8: 2. Classical numerical approaches
A
Jacobi method
B
Gauss–Seidel method
C
Conjugate gradient method

## Slide 9: Jacobi method
First, is split into diagonal and strictly triangular terms: . Then:
This can be discretized to form an iterative update:
In standard Jacobi iteration, you would update per equation, keeping all other equations fixed;

## Slide 10: Jacobi method

## Slide 11: Gauss-Seidel method
Gauss-Seidel is essentially the same but now you use the already computed values.

## Slide 12: Conjugate gradient method
Consider , which will be minimal when its derivative, , is 0.
The simplest minimization method is greedy line search:
Start with an initial point and initial residual .
Pick a direction and compute step size:
Update point
Update residual:
Repeat until convergence.

## Slide 13: Conjugate gradient method
The directions are chosen to be conjugate with respect to .

## Slide 14: Experiment
24 x 24 grid tiling
CG requires fewer iterations.

## Slide 15: 3. Probabilistic numerical approach
A
BayesCG
B
Uncertainty

## Slide 16: BayesCG
Put a prior distribution on the unknown: .
Now pick search directions .
Let for .
This is a Dirac likelihood,
The posterior is then
whose parameters are an update to the prior’s

## Slide 17: BayesCG

## Slide 18: Uncertainty
If you choose and , then the posterior mean is exactly the result of CG.
The posterior variance bounds the error so far.
Every removes a direction of uncertainty.
For , the posterior mean .

## Slide 19: 4. Message passing approach
A
Setup
B
Factor Graphs
C
Belief propagation / Sum-product Message Passing
Notes: Outline
***Setup***
Restate the goal: Want to solve Ax=b for x for given matrix A and vector b. [show Ax=b]
Reference Shantal – “As shown by Shantal et al. there exists a quadratic energy function whose mode encodes the solution to Ax=b - the simple multivariate Gaussian” – [show p(x) ..]
This is shown because where the gradient of log p(x) w.r.t. x equals 0, we find the mode,
and evaluating this gradient, we find it to be equal to -Ax + b. [show grad log px = -Ax +b]
Therefore, the x-configuration at the mode of p(x) is x = A^{-1}b [show x = ..]
“Shantal et al. then also show that the mode could be reliably found by message passing on a probabilistic graph. [
(pass) When A is not PSD, the associated Gaussian is not a proper normalizable probability distribution, but the approach is found to also sometimes work in this case.
If you read their paper, you will find they encode this Gaussian p(x) in a specific type of probabilistic graph known as a Gaussian Markov Random Field. We instead take a more general, modern approach, and encode the same Gaussian in what is called a Forney-style Factor Graph, or FFG.
In either case, message-passing is a scalable, distributed approach to approximate marginal inference. We infer the marginal distributions q(x_i) for each variable x_i in the state vector x. By then stacking the means of these marginals, we can recover the mode of the distribution and thus our solution x = A^{-1}b. Note that we do not recover the complete inverse matrix A^{-1}, only the matrix-vector product, A^{-1}b.
We will now review how to encode this multivariate Gaussian distribution as a factor-graph, and then how to perform message-passing to recover its mode and our solution.
***Factor Graphs***
Factor graphs are easy to understand, and highly useful when it comes to model design.
In short, any arbitrary factorized probabilistic model can be encoded exactly as a factor graph. Consider the model p(a,b,c) = p(a)p(b|a)p(c|b)
This model has a representation as this Forney-style factor-graph, where the nodes denote the factors and the edges denote the variables. The conditional independencies are made vividly clear. This is a simple model and you may argue the algebraic form is just as clear.
However, when we consider a loopy model with arbitrary non-negative factors/potentials f, and normalizing constant Z, such as p(a,b,c,d) = 1/Z f_1(a,b) f_2(b,c) f_3(c,d) f_4(d,a) and this corresponding factor graph, and we see that the loop is readily apparent, whereas in the algebraic form, it is less so, and in more complicated models, model structure can be quite difficult to understand.
And so a factor-graph is a convenient visual representation of a probabilistic model, useful for understanding model structure and formulating message-passing algorithms. Its use becomes even more apparent as we begin to utilize hybrid message-passing approaches, where we apply variational constraints to the variables around specific nodes, and in cases of non-conjugacies, where we may need to apply form-constraints to certain variables that perform projections into conjugate families, etc. For now, we use Gaussian-conjugate factors without variational or form constraints.
We now return to our Gaussian distribution to see how to encode it in a factor-graph for later marginal inference by message-passing. The negative Gaussian function is quadratic and factorizes into unary and binary factors.
We collect and name terms, and we get the model here…
where Phi is…
and Psi is…
Then, assuming a grid-like die structure, we get a graph like so, for example…
Here we pause to review a few more factors that show up frequently in linear Gaussian models. Each have closed-form message rules.
When a variable connects to more than two factors, it gets duplicated via an equality node like this with these rules
Then we have point-mass factors used commonly for measured data, and can be seen to send a mean value without variance.
We have multiplication nodes for multiplication of a variable by a vector or matrix…
We have summation nodes to add or subtract two variables…
And we have a Normal distribution node that forms a Gaussian potential for the output from an input random mean and variance …
***Belief Propagation***
In addition to considering a simple factor graph, we also consider the simplest message-passing formulation, called alternatively Belief-propagation and Sum-product message-passing. Additionally, we perform simple asynchronous message-passing, and I’ll explain what that means.
There are really just two steps to belief propagation that we repeat iteratively until convergence.
The first step is computation of messages, and the second is computation of marginals.
Messages are the local information content about a variable that is sent out from a factor along the edge for that variable, considering that factor’s inputs and factor function. They are functions or potentials of the output variable and need not be normalized, though they often are.
For belief-propagation, the an output message is computed as the integral of the factor function multiplied by all input messages, from variables besides the one for whom we are computing the message. This is shown as so… For Gaussian-conjugate factors and Gaussian messages, these message computations are available in closed-form.
These messages then serve as input to the other factor along that edge.
Asynchronous message-passing then implies that when a factors inputs have changed, it sends out a new message. That’s it.
Second, we compute marginals. We note that the two connected factors both send messages along a variable’s edge. The current iteration’s approximate marginal belief for that variable is the normalized product of those two messages. This is shown as so…
So, factors send messages whenever inputs change, and marginals are computed whenever messages along an edge change.
In a probabilistic model with loops, convergence is not guaranteed, but when it does as it often does in practice, means correspond to the exact posterior marginal means, while covariances are found to be in general, not exact, and often over-confident.
Now we return to our factorized Gaussian model and we showcase the message computation rules for both factors.
For Phi(x_i), only a single message is computed, and as it has no other inputs that might change, it’s outgoing message is computed only once. Evaluating this integral, we find the message to be so…
For Psi(x_i, x_j), the factor is symmetric about x_i and x_j, and so the same message rule is used in either case. It takes the form of this integral, with this closed-form solution… It gets recomputed for x_j whenever the incoming message for x_i changes, and vice-versa.
Finally, for completeness, we display the closed-form product of the two messages along any of these edges that computes the current iterative marginal. That is simply the sum of precision-weighted means and precisions, also known as information vectors and matrices, respectively.

## Slide 20: Message-passing approach: Setup

## Slide 21: Message-passing approach: Factor-graphs

## Slide 22: Message-passing approach: Belief-propagation

## Slide 23: What is a GMRF (Gaussian Markov Random Field)
GMRF = a graph representing a single, multivariate Gaussian
  Vertices encode variables from state-vector
  Edges encode the conditional-independencies in precision matrix, A
  Each also embed local probability factors constraining the variables
We note:
  mode of p(x) is located where
  and because
  -configuration at mode of corresponds to the solution
  and the individual marginals specify that mode

## Slide 24: Factorizing the GMRF to construct the graph
A GMRF is quadratic and factorizes into unary and binary factors
Collecting and naming terms, we get
where
* one example GMRF

## Slide 25: Mean / Marginal inference by message-passing
Message-passing = distributed, approximate marginal inference
  In this case, we use sum-product message-passing
Two iterative steps until convergence:
  send messages between adjacent nodes
  compute marginals at each node
Messages are computed per
Marginals computed per
Analytic update eqs. next slide

## Slide 26: Mean / Marginal inference by message-passing
Define cavity belief at node i (belief at i ignoring j)
Form message from i to j
Obtain current belief for node i
Notes: Cavit is the Gaussian over xi​ formed from the unary factor at i plus all incoming messages except j→i.
Message is a Gaussian information update over xj​, obtained by combining that cavity belief with the coupling ψij​(xi​,xj​) and integrating out xi
Node belief uses all incoming messages, including j→i, and is the current marginal estimate for xi​.

## Slide 27: 5. Stacking modular components
A
B
Building
Anylyzing GaBP (Bayesian Jacobi solver)

## Slide 28: 5. Stacking modular components
A
Anylyzing GaBP (Bayesian Jacobi solver)
B
Building

## Slide 29: Is our generalization useful?
Notes: Rounds to 10⁻¹⁰ on the 24×24 die, c = 0.4: Jacobi 203 · GaBP flooding 112 · Gauss–Seidel 110 · GaBP serial 67 · CG 41.
Same die as Wouter's section: 24×24 lattice, screening 0.4, same right-hand side, same target 1e-10. Jacobi needs 203 iterations. GaBP with the flooding schedule — every node sends every round, exactly Jacobi's communication pattern — needs 112. So the second moment that Jacobi throws away is worth a factor two in rounds. GaBP serial is the same algorithm with a Gauss–Seidel schedule: sweep the nodes in order and let each node use whatever is in its inbox right now, so messages from lower-numbered neighbours are already fresh this sweep. That gets 67 — the same trick Gauss–Seidel plays on Jacobi (110), for the same reason; red–black colouring gives it back at full parallelism, two half-sweeps per round. One round of serial costs the same number of message updates as one round of flooding; only the freshness differs. Say it unprompted: CG is still faster, 41. CG minimises the error over a growing global subspace; a local method has no global object to minimise over. On this problem that is a constant factor, not a change of order — the next two slides make the comparison fair. Also point at the tree: on the chain, GaBP terminates exactly after the diameter; CG does not.

## Slide 30: GaBP is distributed algorithm
Notes: The textbook bound: the A-norm error contracts by (sqrt(kappa)-1)/(sqrt(kappa)+1) per step. For our die kappa = 19.4, which predicts 51 iterations to 1e-10; the measured number is 41. The bound is loose because the spectrum is clustered -- say that, because someone will know it. The honest problem is the second bullet: kappa and ||x*|| are as unknown as the solution, so the bound is not something you can evaluate at run time. And the cost per step is one local matvec plus two global reductions: on P processors that is 2 log2 P barriers per iteration, times 41.

## Slide 31: CG needs global synchronization steps
Notes: The textbook bound: the A-norm error contracts by (sqrt(kappa)-1)/(sqrt(kappa)+1) per step. For our die kappa = 19.4, which predicts 51 iterations to 1e-10; the measured number is 41. The bound is loose because the spectrum is clustered -- say that, because someone will know it. The honest problem is the second bullet: kappa and ||x*|| are as unknown as the solution, so the bound is not something you can evaluate at run time. And the cost per step is one local matvec plus two global reductions: on P processors that is 2 log2 P barriers per iteration, times 41.

## Slide 32: What algorithm wins and for what topology
Notes: The textbook bound: the A-norm error contracts by (sqrt(kappa)-1)/(sqrt(kappa)+1) per step. For our die kappa = 19.4, which predicts 51 iterations to 1e-10; the measured number is 41. The bound is loose because the spectrum is clustered -- say that, because someone will know it. The honest problem is the second bullet: kappa and ||x*|| are as unknown as the solution, so the bound is not something you can evaluate at run time. And the cost per step is one local matvec plus two global reductions: on P processors that is 2 log2 P barriers per iteration, times 41.

## Slide 33: 5. Stacking modular components
A
Bayesian Jacobi solver
B
Building

## Slide 34: Translating from the FFG into Code
Notes: The textbook bound: the A-norm error contracts by (sqrt(kappa)-1)/(sqrt(kappa)+1) per step. For our die kappa = 19.4, which predicts 51 iterations to 1e-10; the measured number is 41. The bound is loose because the spectrum is clustered -- say that, because someone will know it. The honest problem is the second bullet: kappa and ||x*|| are as unknown as the solution, so the bound is not something you can evaluate at run time. And the cost per step is one local matvec plus two global reductions: on P processors that is 2 log2 P barriers per iteration, times 41.

## Slide 35: Adding a time hierarchy
Notes: The textbook bound: the A-norm error contracts by (sqrt(kappa)-1)/(sqrt(kappa)+1) per step. For our die kappa = 19.4, which predicts 51 iterations to 1e-10; the measured number is 41. The bound is loose because the spectrum is clustered -- say that, because someone will know it. The honest problem is the second bullet: kappa and ||x*|| are as unknown as the solution, so the bound is not something you can evaluate at run time. And the cost per step is one local matvec plus two global reductions: on P processors that is 2 log2 P barriers per iteration, times 41.

## Slide 36: A linear state space model is a probabilistic block
Notes: The textbook bound: the A-norm error contracts by (sqrt(kappa)-1)/(sqrt(kappa)+1) per step. For our die kappa = 19.4, which predicts 51 iterations to 1e-10; the measured number is 41. The bound is loose because the spectrum is clustered -- say that, because someone will know it. The honest problem is the second bullet: kappa and ||x*|| are as unknown as the solution, so the bound is not something you can evaluate at run time. And the cost per step is one local matvec plus two global reductions: on P processors that is 2 log2 P barriers per iteration, times 41.

## Slide 37: A linear state space in code
Notes: The textbook bound: the A-norm error contracts by (sqrt(kappa)-1)/(sqrt(kappa)+1) per step. For our die kappa = 19.4, which predicts 51 iterations to 1e-10; the measured number is 41. The bound is loose because the spectrum is clustered -- say that, because someone will know it. The honest problem is the second bullet: kappa and ||x*|| are as unknown as the solution, so the bound is not something you can evaluate at run time. And the cost per step is one local matvec plus two global reductions: on P processors that is 2 log2 P barriers per iteration, times 41.

## Slide 38: Compositional payoff
Notes: The textbook bound: the A-norm error contracts by (sqrt(kappa)-1)/(sqrt(kappa)+1) per step. For our die kappa = 19.4, which predicts 51 iterations to 1e-10; the measured number is 41. The bound is loose because the spectrum is clustered -- say that, because someone will know it. The honest problem is the second bullet: kappa and ||x*|| are as unknown as the solution, so the bound is not something you can evaluate at run time. And the cost per step is one local matvec plus two global reductions: on P processors that is 2 log2 P barriers per iteration, times 41.

## Slide 39: Let's do some Infer!
Notes: The textbook bound: the A-norm error contracts by (sqrt(kappa)-1)/(sqrt(kappa)+1) per step. For our die kappa = 19.4, which predicts 51 iterations to 1e-10; the measured number is 41. The bound is loose because the spectrum is clustered -- say that, because someone will know it. The honest problem is the second bullet: kappa and ||x*|| are as unknown as the solution, so the bound is not something you can evaluate at run time. And the cost per step is one local matvec plus two global reductions: on P processors that is 2 log2 P barriers per iteration, times 41.

## Slide 41: Extra: convergence of Jacobi iteration
Jacobi updates are a fixed-point iteration with iteration matrix .
It can be shown that it converges for every if and only if the spectral radius
Take, for example, a chain tiling of the die such that A is tridiagonal with values .
Then, the eigenvalues of are for .
This means the spectral radius is , which is roughly and less than 1.

## Slide 42: Extra: error rates
For , the error rate of the conjugate gradient method is

## Slide 43: Extra: CG is posterior mean of BayesCG
If you choose and , then the posterior mean is exactly the result of CG: